## Slide 1: IIR&FIR Filter – VGA – Audio synchronized Lights
Kian David Warias
Advanced Digital Systems
ECET 349
Final Project

## Slide 2: Introduction What is the project about. A technical overview.
3 Filters : IIR – low and high pass for treble and bass enhancement
FIR – moving average filter
8 LED’s : Display music output with 8 LEDs on DE1 board
VGA : Display current selected filter on VGA screen
filter0
Media Input
Selected Filter
Music synchronized LEDs
Select filter typ; activate LEDs

## Slide 3: Design approach
Cost considerations
VGA TO VGA Cable & Stereo Audio Aux Cable
$119
VGA TO VGA Cable & Stereo Audio Aux Cable
$12.31
$131.31

## Slide 4: Design approach
Implemented features:
3 Filters :
IIR – low pass for bass enhancement
IIR – high pass for treble enhancement
FIR – moving average filter
8 green LEDs
Displays music output with 8 LEDs on DE1 Board
VGA
Display current selected filter on VGA screen
extend FSM from Lab9 using seperate states for each filter
Indicate selected filter/state on red LEDs.
- use code from Lab11
- change code that the memory can hold two more images.
- new Entity which uses the filter output

## Slide 5: Challenges & Issues
encountered during implementation and how they were solved. Indicate how many hours you spent working on this project and the cost of any peripherals that were used.
Challenge / Issue | Solution
Implement more than one filter in filter_fsm | I extended the given fsm from Lab 9 with three additional states. A state to select the other three filter states, called filter_select. And seperate states for each filter, called filter0, filter1, filter2.
Display/Store more than one image in ROM for VGA Output | The shown image depends on the selected filter, triggerd by the switches SW1 to SW3. The used images are saved in new implemented “rom” signals of type “memory”.
Synchronize music with lights | I created new entity which breaks down the 16-bit input (left_out & right_out from filter_fsm) into a 8-bit width output vector.  I am not statisfyed with the current Solution. The function of a „real“ audio peak meter is not given yet.
I spent a whole day working on the FSM without hearing a difference after compiling. | Select correct file path (outputfile) in Progammer.

## Slide 6: Block Diagram Overview
Input filter and Music synchronized Lights
INPUT
VGAOUT
LED OUT
AUXOUT
Switches
&
Reset
AUX IN
Show selected filter on Monitor
LEDG0 – LEDG7
VGA
LINE IN
LINE OUT
DE1 Board

## Slide 7: Block Diagram detailed Overview
ENTITY INCLUDES FILTER FSM WITH 3 FILTERS
filter_fsm
ENTITY
VISUALIZE PLAYED AUDIO
Audio_to_Led
ENITIES HANDEL MUSIC IN-&OUTPUT
Stream_codec
&
Stream_codec
ENTITIES DISPLAY CURRENT FILTER STATE
vga_640x480
&
vga_stripe_rom
INPUT
VGAOUT
LED OUT
AUXOUT
AUX
IN
(SW, RST, CLK)
DE1 Board

## Slide 8: Block Diagram more detailed Overview
filter_fsm
Audio_to_Led
Stream_codec
i2c_codec
vga_640x480
vga_stripe_rom
SW
IN
VGAOUT
LED OUT
AUX IN&OUT
CLK
clk_div
clk_div_VGA
RST
All Entities are using the same reset!
Not all clk connections are shown!
DE1 Board

## Slide 9: Block Diagram completed Schematic File (top.bdf)

## Slide 10: Validation
filter0
AUX Input
eg. connect with your PCs headphone output
Monitor shows selected Filter
LEDG0 –LEDG7
Displays Music synchronized Lights
Switches:
SW0  Music on/off
SW1  treble enhancement
SW2  bass enhancement
SW3  moving average filter
SW4  LEDG0 –LEDG7 on/off
VGA cable from DE1 Board to Monitor
VGA Output
RESET
AUX Output
to speaker

## Slide 11: Conclusion
Why do it? - Societal relevance/impact and opportunity for commercialization
What you learned from this project? - Learning Outcomes